## Slide 1: Dokumentasjon til operatører
Innspill dialogkonferanse - Ruter

## Slide 2: Oslo syd

## Slide 3
All calculations are estimates by Ruter. Applicants must perform their own calculations.

## Slide 4: Line 18N

## Slide 6: Line 18n – Subset of stops
Table shows subset of stops on line

## Slide 7: Line 18n – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
18N Tur/retur |  |  | 70,5 | 27704 | 1,53 |  | 120
18N Tur | Åsbråten | Kringsjå | 41 | 23343 | 1,8 | 96 | 60
18N Retur | Kringsjå | Åsbråten | 29,5 | 23343 | 1,26 | -96 | 60
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 8: Line 73

## Slide 10: Line 73 – Subset of stops
Table shows subset of stops on line

## Slide 11: Line 73 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
73 Tur/retur |  |  | 17,4 | 12984 | 1,34 |  | 40
73 Tur | Pasop | Holmlia stasjon | 7,2 | 6492 | 1,1 | -67 | 20
73 Retur | Holmlia stasjon | Pasop | 10,2 | 6492 | 1,57 | 67 | 20
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 12: Line 77

## Slide 14: Line 77 – Subset of stops
Table shows subset of stops on line

## Slide 15: Line 77 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
77 Tur/retur |  |  | 22,7 | 17348 | 1,3 |  | 42
77 Tur | Langteigåsen | Holmlia stasjon | 14,0 | 8674 | 1,0 | -109 | 21
77 Retur | Holmlia stasjon | Langteigåsen | 8,7 | 8674 | 1,6 | 109 | 21
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 16: Line 77B

## Slide 18: Line 77B – Subset of stops
Table shows subset of stops on line

## Slide 19: Line 77B – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
77B Tur/retur |  |  | 2,9 | 2590 | 1,14 |  | 6
77B Tur | Asperudåsen | Holmlia stasjon | 1,1 | 1295 | 0,9 | -13 | 3
77B Retur | Holmlia stasjon | Asperudåsen | 1,8 | 1295 | 1,37 | 13 | 3
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 20: Line 77C

## Slide 21: Line 77X

## Slide 23: Line 77x – Subset of stops
Table shows subset of stops on line

## Slide 24: Line 77X – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
77X Tur/retur |  |  | 12,2 | 9094 | 1,3 |  | 22
77X Tur | Bjørndal | Hauketo stasjon | 3,3 | 4547 | 0,7 | -124 | 11
77X Retur | Hauketo stasjon | Bjørndal | 8,9 | 4547 | 1,9 | 124 | 11
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 25: Line 79

## Slide 27: Line 79 – Subset of stops
Table shows subset of stops on line

## Slide 28: Line 79 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
79 Tur/retur |  |  | 85,7 | 53582 | 1,6 |  | 142
79 Tur | Grorud T | Åsbråten | 40,1 | 26791 | 1,5 | -97 | 71
79 Retur | Åsbråten | Grorud T | 45,6 | 26791 | 1,7 | 97 | 71
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 29: Line 80E

## Slide 31: Line 80E – Subset of stops
Table shows subset of stops on line

## Slide 32: Line 80e – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
80E Tur/retur |  |  | 42,0 | 25760 | 1,6 |  | 62
80E Tur | Jernbanetorget | Åsbråten | 24,1 | 13780 | 1,8 | 92 | 31
80E Retur | Åsbråten | Jernbanetorget | 17,9 | 13780 | 1,3 | -92 | 31
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 33: Line 81

## Slide 35: Line 81 – Subset of stops
Table shows subset of stops on line

## Slide 36: Line 81 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
81 Tur/retur |  |  | 75,5 | 51626 | 1,5 |  | 112
81 Tur | Fornebu vest | Fløysbonn | 43,0 | 25813 | 1,7 | 142 | 56
81 Retur | Fløysbonn | Fornebu vest | 32,5 | 25813 | 1,3 | -142 | 56
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 37: Line 82E

## Slide 39: Line 82E – Subset of stops
Table shows subset of stops on line

## Slide 40: Line 82e – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
82E Tur/retur |  |  | 46,3 | 32580 | 1,4 |  | 62
82E Tur | Tårnåsen | Jernbanetorget | 19,7 | 16290 | 1,2 | -152 | 31
82E Retur | Jernbanetorget | Tårnåsen | 26,6 | 16290 | 1,6 | 152 | 31
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 41: Line 83

## Slide 43: Line 83 – Subset of stops
Table shows subset of stops on line

## Slide 44: Line 83 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
83 Tur/retur |  |  | 63,2 | 45768 | 1,4 |  | 94
83 Tur | Tårnåsen | Jernbanetorget | 29 | 22884 | 1,3 | -152 | 47
83 Retur | Jernbanetorget | Tårnåsen | 34,2 | 22884 | 1,5 | 152 | 47
Energy calculations are based on:
- Physics simulation of actual route
- 18 m bus, with total weight of 24,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 45: Line 85

## Slide 47: Line 85 – Subset of stops
Table shows subset of stops on line

## Slide 48: Line 85 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
85 Tur/retur |  |  | 24,2 | 19086 | 1,3 |  | 50
85 Tur | Ulvøya | Jernbanetorget | 11,5 | 9543 | 1,2 | -22 | 25
85 Retur | Jernbanetorget | Ulvøya | 12,7 | 9543 | 1,3 | 22 | 25
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 49: Line 87

## Slide 51: Line 87 – Subset of stops
Table shows subset of stops on line

## Slide 52: Line 87 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
87 Tur/retur |  |  | 38,2 | 28772 | 1,35 |  | 70
87 Tur | Hauketo stasjon | Vevelstad stasjon | 19,6 | 14386 | 1,4 | 39 | 35
87 Retur | Vevelstad stasjon | Hauketo stasjon | 18,6 | 14386 | 1,3 | -39 | 35
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 53: Line 580

## Slide 55: Line 580 – Subset of stops
Table shows subset of stops on line

## Slide 56: Line 580 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
580 Tur/retur |  |  | 34,1 | 26510 | 1,3 |  | 66
580 Tur | Oppegård rådhus | Fugleåsen | 18,9 | 13255 | 1,4 | 45 | 33
580 Retur | Fugleåsen | Oppegård rådhus | 15,2 | 13255 | 1,2 | -45 | 33
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking

## Slide 57: Line 585

## Slide 59: Line 585 – Subset of stops
Table shows subset of stops on line

## Slide 60: Line 585 – Energy calculations
Line | Start | Stop | Energy [kWh] | Distance [m] | Energy per distance [kWh/km] | Altitude difference [m] | Time [min]
585 Tur/retur |  |  | 32,3 | 22878 | 1,43 |  | 44
585 Tur | Kolbotn skole | Svartskog | 15,5 | 11439 | 1,4 | -33 | 22
585 Retur | Svartskog | Kolbotn skole | 16,8 | 11439 | 1,5 | 33 | 22
Energy calculations are based on:
- Physics simulation of actual route
- 12 m bus, with total weight of 17,5 tons (including passengers)
- 50 % efficiency of regenerative braking