## Slide 1
Regulatory Perspective on Platelets and Platelet-like Products
BARDA State of the Technology Meeting
February 19, 2026
Carlos H. Villa, MD PhD
Clinician Investigator, Versiti Blood Research Institute
Clinical Consultant, Versiti Diagnostic Labs

## Slide 2: Overview
Regulatory history and framework for platelets
  Knowledge gaps
Platelets and platelet-like products as:
  Biologics
  Output of medical devices
  Drugs
Clinical development and regulation

## Slide 3: Disclaimer - Things I Learned at FDA
Specifics of FDA’s regulatory approach to a given product is likely to depend on a product-specific assessment, including potential benefits and risks
Sponsors and stakeholders with questions on their specific product or plans for clinical development should contact FDA
Engagement with regulatory authorities throughout the product lifecycle is in everyone’s best interests
  ‘There’s a guidance for everything’

## Slide 4: Blood and blood components are biologics
Defined in the Public Health Service Act Section 351
  Virus, therapeutic serum, toxin, antitoxin, vaccine, blood, blood component or derivative, allergenic product, protein (except any chemically synthesized polypeptide), or analogous product… applicable to the prevention, treatment, or cure of a disease or condition of human beings.
Under PHSA/FD&C, biologics and drugs must be licensed or approved to introduce into interstate commerce
  Product is safe, pure, and potent
Notes: Outcome of a successful biologics license application (BLA)
The biologic product (including blood or blood components) is safe, pure, and potent
The facility in which the biological product is manufactured, processed, packed, or held meets appropriate standards

## Slide 5: Biologics also meet the definition of drugs
Also subject to certain provisions of the Federal Food Drug and Cosmetics Act, including regulations governing:
  Good manufacturing practice, “GMPs”
  Labeling
  Misbranding
  Adulteration
  Civil and criminal penalties
Among others…

## Slide 6: Historical context
United States v. Calise 217 F.Supp. 705 (1962)
United States v. Steinschreiber, 219 F. Supp. 373 (S.D.N.Y. 1963)
Images: Charleston Gazette 1/26/1962; Gettysburg Times 7/3/1963
Notes: First prosecution and criminal conviction under the “biological products” provisions of the Public Health Service Act
The trial court found them guilty, establishing precedent that blood products, even whole blood, fell under federal biological product regulations, a point clarified in subsequent related cases like United

## Slide 7: Unique Aspects of Blood and Blood Components
General regulations for biologics are described in 21 CFR 600, but there are several regulations specifically relevant to blood and blood components, including Platelets:
  21 CFR 606: Current good manufacturing practice for blood and blood components
  21 CFR 607: Registration and product listing
  21 CFR 630: Requirements for blood and blood components intended for transfusion or further manufacturing
  21 CFR 640: Additional standards for blood and blood components
Notes: 21 CFR 606.122 – Circular of Information
21 CFR 606.145 – Control of bacterial contamination of platelets
21 CFR 607.65 – Exemptions for blood product establishments
21 CFR 630.10 – General donor eligibility requirements
21 CFR 640.60 – definitions and standards for WB, RBC, plasma, platelets

## Slide 8: Platelets in the CFR
Platelets and additional relevant standards are defined under 21 CFR 640 Part C
  Eligibility of donors
  Frequency of donation
  Collection of source material
  Testing the blood
  Processing
  General requirements
Regulations established in 1975 (40 FR 4304) and revised several times thereafter

## Slide 9: Old questions persist…
“Since platelets maintain their therapeutic viability for only a brief period of time, there is differing medical opinion with respect to appropriate storage temperatures. Platelets stored at 20-24° C exhibit a longer post-transfusion survival time than platelets stored between 1-6° C. which, on the other hand, appear to be more potent during the initial stages of producing hemostasis. Both of these qualities are desirable. Thus, the Commissioner proposes that a licensed manufacturer may store the product at either temperature and utilize processing, labeling and distributing procedures consistent with each.”
- Federal Register, 1974 (39 FR 2008)

## Slide 10: Indications for Platelets
Defined in the Circular of Information (most commonly the FDA-recognized AABB/ARC/ABC/ASBP https://www.fda.gov/media/86898/download )
“… patients with thrombocytopenia, dysfunctional platelet disorders (congenital, metabolic, or medication-induced), or active platelet-related bleeding, or patients at serious risk of bleeding (ie, prophylactic use). … Patients undergoing extracorporeal membrane oxygenation or cardiopulmonary bypass may also need platelet transfusion, and platelets are frequently indicated in massive transfusion protocols”
Very broad compared to typical drug labeling  historical

## Slide 11: The effectiveness challenge for platelets

## Slide 12
Platelet transfusions are standard of care in many clinical settings where well-controlled studies are limited or absent
Simon J. Stanworth, Akshay Shah; How I use platelet transfusions. Blood 2022; 140 (18): 1925–1936.

## Slide 13
Platelet transfusions are standard of care in many clinical settings where well-controlled studies are limited or absent
Simon J. Stanworth, Akshay Shah; How I use platelet transfusions. Blood 2022; 140 (18): 1925–1936.
Often not factored into clinical transfusion decisions or study designs

## Slide 14: Liberal vs restrictive
Many/most studies designed to answer the question of if it is OK to transfuse less platelets (restrictive vs liberal) rather than should we transfuse any platelets (true efficacy study)
  Metcalf RA, Nahirniak S, Guyatt G, et al. Platelet Transfusion: 2025 AABB and ICTMG International Clinical Practice Guidelines. JAMA. 2025;334(7):606–617. doi:10.1001/jama.2025.7529
  Jug R, La Rocca U, Al-Riyami AZ, Bathla A, Metcalf RA, White SK, Stanworth SJ, Nahirniak S. The clinical use of platelet transfusions: A systematic literature review and meta-analysis on behalf of the International Collaboration for Transfusion Medicine Guidelines. Transfusion. 2025 Jun;65(6):1155-1169. doi: 10.1111/trf.18277.
What does this mean for regulatory development?
  Need to consider control arm carefully
Notes: Many/most studies designed to answer the question of if it is OK to transfuse less platelets rather than should we transfuse any platelets
Complicates comparison to standard-of-care when platelet transfusion is considered standard of care, particularly non-inferiority designs, or where product is meant to substitute for platelets

## Slide 15: Endpoints: a study design challenge for platelets
Depends on clinical population and indications (get regulatory authority feedback)
Clinical benefit: A positive clinically meaningful effect of an intervention on how the patient feels, functions, or survives
  A comparative advantage in treatment of the disease or a comparative reduction in treatment-related toxicity
Although diverse roles in normal physiology, platelets as a therapeutic agent are typically considered for treatment or prevention of bleeding
Notes: Regulatory standard is feels, functions, or survives

## Slide 16: Bleeding endpoint considerations
Optimal bleeding endpoints and outcomes are not definitively established
September 2019 NIH/NHLBI Consensus Conference
  Spinella PC, et al. Hemostasis Trials Outcomes Working Group. Recommended primary outcomes for clinical trials evaluating hemostatic blood products and agents in patients with bleeding: Proceedings of a National Heart Lung and Blood Institute and US Department of Defense Consensus Conference. J Trauma Acute Care Surg. 2021 Aug 1;91(2S Suppl 2):S19-S25.
Ex: WHO Grade 2 or higher bleeding in hypo-proliferative thrombocytopenia
Notes: GI bleeding, hypo-proliferative thrombocytopenia, cardiac surgical bleeding, intracranial hemorrhage

## Slide 17
Platelets
Medical
Devices
Platelet-like
Products
?

## Slide 18
Platelets
Medical
Devices
Platelet-like
Products

## Slide 19: Manufacturing Platelets as a Blood Component
Platelets intended for transfusion are generally manufactured by blood establishments and may be subject to additional processing steps
Processes carried out by blood establishments in the manufacture of platelets are relatively simple
  Use cleared or approved medical devices in accordance with their instructions for use
Examples include leukocyte reduction, irradiation, dividing the product, pathogen reduction

## Slide 20: Licensure of Platelets
Establishments must comply with requirements regarding establishment registration and product listing
Blood establishments must not introduce platelets into interstate commerce without a BLA
“Registered-only” establishments must still comply with applicable regulations

## Slide 21: Blood establishment licensure
Blood establishments seeking to license Platelets submit data to support the safety, purity, and potency of the components:
  Examples include qualification of the collection process, quality assurance procedures, processing and testing, and labeling
  QC requirements for count, pH, and volume (21 CFR 640.25(b))

## Slide 22: Platelet Guidance Documents
In addition to regulations, FDA issues guidance documents that provide blood establishments with recommendations on the manufacture of Platelets (and other blood components)
  https://www.fda.gov/vaccines-blood-biologics/biologics-guidances/blood-guidances
Examples:
  Collection of Platelets by Automated Methods
  Alternative Procedures for the Manufacture of Cold-Stored Platelets Intended for the Treatment of Active Bleeding when Conventional Platelets Are Not Available or Their Use Is Not Practical
  Bacterial Risk Control Strategies for Blood Collection Establishments and Transfusion Services to Enhance the Safety and Availability of Platelets for Transfusion

## Slide 23
Platelets
Medical
Devices
Platelet-like
Products
?

## Slide 24
Platelets
Medical
Devices
Platelet-like
Products

## Slide 25
Platelets
Medical
Devices
Platelet-like
Products

## Slide 26: Devices can be used to process or store Platelets

## Slide 27: Device Paradigm
Blood establishments that manufacture Platelets must use approved or cleared medical devices in a manner consistent with the instructions provided by the manufacturer
Regulatory classes of devices are based on the level of control necessary to assure the safety and effectiveness of the device
  Class I (lowest risk), Class II (moderate risk), Class III (highest risk)
Class to which a device is assigned determines, among other things, the type of premarketing submission/application required for FDA clearance to market

## Slide 28: What data for a device?
Design and materials
Methods and controls used for manufacture
Biocompatibility (extractables and leachables)
Performance data (e.g., sterilization, closure integrity)
In vitro platelet parameters
May be useful to review recent guidance “Recommendations for the Development of Blood Collection, Processing, and Storage Systems for the Manufacture of Blood Components Using the Buffy Coat Method” (draft) https://www.fda.gov/media/182751/download

## Slide 29: Do I need clinical studies?
If a device is used to process or store Platelets intended for transfusion, it is still possible that clinical studies of the Platelets will be needed to support clearance or approval of the device
  Pathogen reduction devices and pathogen-reduced Platelets
  Storage devices and cold stored platelet dating period
Regulatory interaction through the Q submission process:
https://www.fda.gov/media/114034/download

## Slide 30: n.b., additive solutions may be regulated as drugs (NDA pathway)

## Slide 31
Platelets
Medical
Devices
Platelet-like
Products
?

## Slide 32
Platelets
Medical
Devices
Platelet-like
Products

## Slide 33: Platelet-like Products
Platelets may be subjected to further manufacturing using complex processes
  Can result in a product sufficiently different from Platelets such that it would likely be regulated as a novel biologic (or combination) product
  The scientific understanding of the effects and risks of Platelets do not necessarily apply to the final “Platelet-like” product
Synthetic or semi-synthetic approaches may be used to manufacture products that mimic aspects of platelet function
  Generally, these are entirely new products (e.g., drugs, biologics, or combination products)
Combination product: pathway and jurisdiction based on a determination of the “primary mode of action”
Notes: primary mode of action as “the single mode of action of a combination product that provides the most important therapeutic action of the combination product” (see also definitions at 21 CFR 3.2. In some cases, the most important therapeutic action cannot be determined. For example, a combination product may have two independent modes of action, neither of which is subordinate to the other. To resolve these types of questions, FDA’s regulations at 21 CFR Part 3 include an algorithm for determining center assignment. The algorithm directs center assignment based on which center regulates combination products raising similar types of safety and effectiveness questions, or, if there is no such center, based on which center has the most expertise to evaluate the most significant safety and effectiveness questions raised by the combination product.

## Slide 34: Platelets and Platelet-like Products
Platelets are regulated by the Office of Blood Research and Review at CBER
Biologic platelet-like products are generally regulated at CBER
  May be OBRR or OTP
Certain synthetic platelet mimetics may be regulated by CDER
  Other centers or offices may provide consultative input

## Slide 35: How do you license or approve a novel platelet-like product?
Products typically follow a “lifecycle” to transition from pre-clinical phase to clinical investigation and ultimately to licensure (biologic) or approval (drug)
  IND = “Investigational New Drug” (21 CFR 312)
Communication with FDA occurs throughout the process
Details of a product “lifecycle” can be very product specific
Notes: a novel component with a new indication for use
examples of types of products

## Slide 36: Indications and Usage of Platelet-like Products
Expect these would overlap with clinical settings where Platelets are transfused:
  Hypo-proliferative thrombocytopenia
  Cardiac surgery with platelet dysfunction or thrombocytopenia
  Other perioperative bleeding
  Traumatic hemorrhage
Expect that clinical studies to support licensure or approval will depend on characteristics of the product and indications being sought
  Recommend early regulatory interaction – labeling will likely be more specific compared to COI for blood components

## Slide 37: What is potency and why do we need it?

## Slide 38: Potency
“the specific ability or capacity of the product, as indicated by appropriate laboratory tests or by adequately controlled clinical data obtained through the administration of the product in the manner intended, to effect a given result.” (21 CFR 600.3(s))
Why test?
  It’s required under regulation (e.g., 21 CFR 610.10)
  Informs many facets of CGMP, conformance testing, comparability studies, stability testing, manufacturing
Used during all phases of clinical study
Notes: Lot release
Stability evaluation
In-use studies and delivery device compatibility studies
Comparability studies
Manufacturing process studies – how manufacturing step changes affect potency
Implications

## Slide 39: Potency problem for Platelets and platelet-like products
Small lots (n=1?), donor variability
Lab tests are limited
  Currently use count together with circulatory recovery and survival, and other in vitro parameters for Platelets
What about hemostatic agents?
  TGA?
Need to develop/qualify/validate assays that better correlate with or predict clinical outcomes
  Products and patients
  When during development? The earlier, the better
Depasse, F et al. Journal of Thrombosis and Haemostasis. 2021 19(12): 2907 - 2917
Cancelas JA, et al. Transfusion. 2022 Aug;62(8):1619-1629.
Notes: No definitive lab test that predicts hemostatic effectiveness
Circulatory recovery and survival and various in vitro measurements are currently used for Platelets
Several have been proposed for hemostatic agents  e.g., thrombin generation assay

## Slide 40: The “Lifecycle” of a Biologic Product or Drug
Pre-IND
IND Review
BLA / NDA
Post-Licensure
Phase 1
Phase 2
Phase 3
‘Discovery/
Preclinical’
Meeting types:
INTERACT
Pre-IND
‘Clinical development’
Phase 1 – Safety
Phase 2 – Safety; Dose Finding; preliminary efficacy
Phase 3 – Safety; Efficacy
Regulatory interactions throughout (e.g., End-of-phase meetings)
Data to support approval
Inspection
Lot Release
Safety monitoring
Phase 4 studies
Notes: The clinical investigation of a previously untested drug is generally divided into three phases. Although in general the phases are conducted sequentially, they may overlap.

## Slide 41: Pre-IND Phase (‘Preclinical’ development)
INTERACT – Initial Targeted Engagement for Regulatory Advice on CBER/CDER Products
  Early interaction, initial nonbinding advice
  Example topics: Requirements for preclinical testing, aspects of manufacturing for “first-in-human” trials
Pre-IND
  Advice prior to submission of Investigational New Drug (IND) application
  Direct interaction/discussion and identify potential clinical hold issues
https://www.fda.gov/vaccines-blood-biologics/industry-biologics/interact-meetings-initial-targeted-engagement-regulatory-advice-cber-products
Notes: preliminary informal consultation with the Agency at an early stage of development prior to a pre-IND meeting, subject to Agency resource constraints.

## Slide 42: IND Phases of Clinical Investigation
Varies considerably by product
Often overlapping phases
 | Phase 1 | Phase 2 | Phase 3
Goal | Evaluate safety and side effects | Evaluate safety, explore efficacy, and dosing | Obtain evidence of efficacy and safety for regulatory approval
Design Considerations | Typically dose-escalation, safety endpoints | Highly variable | Powered for efficacy and safety assessments; Prespecified statistical criteria
Population | Often healthy subjects, typically smallest studies | Subjects with disease/condition | Closest to target population

## Slide 43: Important Aspects of IND Review
FDA’s primary objectives in reviewing an IND are to assure the safety and rights of subjects
Depending on the phase of the study, objectives may also include assurance of the quality of the scientific evaluation of biologics to permit evaluation of drug’s effectiveness and safety (21 CFR 312.22)
IND applications are allowed to proceed or placed on clinical hold
  30 days from submission
  Grounds for clinical hold described under 21 CFR 312.42
Notes: Human subjects are or would be exposed to an unreasonable and significant risk of illness or injury
The clinical investigators are not qualified by reason of their scientific training and experience
The investigator brochure is misleading, erroneous, or materially incomplete
(iv) The IND does not contain sufficient information to assess the risks to subjects of the proposed studies.
(v) Study for a life-threatening disease that affects both genders, and trial excludes based on gender
Phase II/III: The plan or protocol for the investigation is clearly deficient in design to meet its stated objectives

## Slide 44: Expedited review pathways
Described under Section 506 of the Food, Drug, and Cosmetic Act (FD&C Act)
  https://www.fda.gov/regulatory-information/search-fda-guidance-documents/expedited-programs-serious-conditions-drugs-and-biologics
Types of formal expedited review pathways:
  Fast Track
  Breakthrough Therapy
  Accelerated Approval
  Priority Review
Notes: Fast track – facilitate development and expedite review (serious condition and unmet need…no current therapy, advantages over available therapy); more frequent meetings, rolling review
Breakthrough – expedite development and review (serious condition and preliminary clinical evidence indicates that the drug may demonstrate substantial improvement over available therapy [ can include surrogate endpt]); gets all fast track + intensive guidance + organizational commitment
Accelerated approval - drugs for serious conditions that filled an unmet medical need to be approved based on a surrogate endpoint, will still need phase 4 confirmatory trials.
Priority review - would be significant improvements in the safety or effectiveness of the treatment, diagnosis, or prevention of serious conditions when compared to standard applications.; shorter review clock 6 months

## Slide 45: Expanded access programs
Sometimes called “compassionate use”
For patients with immediately life-threatening condition or serious disease to gain access to investigational medical product outside of clinical trial when no satisfactory alternative options are available (21 CFR 312.305)
  Individual patients, including emergency use (21 CFR 312.310)
  Intermediate-size patient populations (21 CFR 312.315)
  Treatment IND (21 CFR 312.320)
https://www.fda.gov/regulatory-information/search-fda-guidance-documents/expanded-access-investigational-drugs-treatment-use-questions-and-answers

## Slide 46: Thank you!
Former colleagues at FDA, CBER, and OBRR
Colleagues at Versiti
Symposium sponsors, organizers, and support staff
  CCCRP, BARDA, DHA, MTEC
  Toby Silverman, MD, MPH
  Andre Cap, MD, PhD

## Slide 47: Bibliography
Simon J. Stanworth, Akshay Shah; How I use platelet transfusions. Blood 2022; 140 (18): 1925–1936.
Metcalf RA, Nahirniak S, Guyatt G, et al. Platelet Transfusion: 2025 AABB and ICTMG International Clinical Practice Guidelines. JAMA. 2025;334(7):606–617. doi:10.1001/jama.2025.7529
Jug R, La Rocca U, Al-Riyami AZ, Bathla A, Metcalf RA, White SK, Stanworth SJ, Nahirniak S. The clinical use of platelet transfusions: A systematic literature review and meta-analysis on behalf of the International Collaboration for Transfusion Medicine Guidelines. Transfusion. 2025 Jun;65(6):1155-1169. doi: 10.1111/trf.18277.
Spinella PC, et al. Hemostasis Trials Outcomes Working Group. Recommended primary outcomes for clinical trials evaluating hemostatic blood products and agents in patients with bleeding: Proceedings of a National Heart Lung and Blood Institute and US Department of Defense Consensus Conference. J Trauma Acute Care Surg. 2021 Aug 1;91(2S Suppl 2):S19-S25.
FDA Blood Guidance Documents: https://www.fda.gov/vaccines-blood-biologics/biologics-guidances/blood-guidances
FDA INTERACT Meetings: https://www.fda.gov/vaccines-blood-biologics/industry-biologics/interact-meetings-initial-targeted-engagement-regulatory-advice-cber-products
FDA Q Submission: https://www.fda.gov/media/114034/download
FDA Expedited Programs: https://www.fda.gov/regulatory-information/search-fda-guidance-documents/expedited-programs-serious-conditions-drugs-and-biologics
FDA Expanded Access: https://www.fda.gov/regulatory-information/search-fda-guidance-documents/expanded-access-investigational-drugs-treatment-use-questions-and-answers