## Slide 1: RDS4X
RDS4X.org
Yann CHAPELLE (yann.y.chapelle.external@airbus.com)
Thomas BARRE (thomas.barre@airbus.com)
Let’s demonstrate the added value of ISO/IEC 81346 (RDS)
24-02-2026

## Slide 2: Content of this Presentation
Draft of our WHY HOW WHAT communication kit
Next steps?
First usecase overview

## Slide 3: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 4: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 5: Why?
Increasing amount of data is unmanageable
Lack of meaning and context
Disparate softwares and storage solutions create data silos
AS IS

## Slide 6: Why?
Scalability of data management
Explicit and contextualized data
Reliability and accessibility ensured by data continuity
TO BE

## Slide 7: Why?
We believe in a Common Language for…
To help us design, build, operate, and maintain even the most complex projects
Universal Understanding
Universal Understanding
Future-Proof Consistency
Future-Proof Consistency
Seamless Interoperability
Seamless Interoperability

## Slide 8: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 9: How? | The Reference Model
Introduction of a Reference Model that…
Acts as the semantic bridge that aligns different softwares
Provides the essential structure for data, ensuring information is born "intelligent" and contextualized

## Slide 10: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 11: What is a spoiler?
A spoiler is a device which increases the drag and decreases the lift of an airfoil in a controlled way
But not only…
Speed brake?
Spoiler?

## Slide 12: What is a spoiler?
It is a very complex system that links the pilot to the airflow
Let’s use RDS 81346 to address this challenge!
We need a reference model
How can we clarify and explicit this complexity unambiguously?
How can we take into account its various aspects?

## Slide 13: Full Reference Model

## Slide 14: Collaboration across vehicle industrials
DNV will demonstrate the applicability of Part 20 for ships
Integration in the Reference Model as transporter between facilities

## Slide 15: Physical Aspect – Logical View
Using part 20 - Vehicles and part 2 - Components with Product Aspect
Systems are directly linked to RDS and its definitions
CF – technical system designed to control fluid dynamics by modifying it by active means
UPB – object holding other objects by non-static mechanical jointing
ULN – object for structurally holding other objects in the form of a plane or curved surface withstanding tensile forces
QNA – object for controlling the variation of flow of liquid in sealed enclosures
MMA – object for providing mechanical movement or force powered by fluid displacement or pressure providing movement corresponding to a liquid volume

## Slide 16: Physical Aspect – BOM
The logical physical view is linked to the Bill of Materials that realizes it
ULN – object for structurally holding other objects in the form of a plane or curved surface withstanding tensile forces
MMA – object for providing mechanical movement or force powered by fluid displacement or pressure providing movement corresponding to a liquid volume
What we assemble
What we buy

## Slide 17: Functional Aspect
RDS provides a common language for both technical teams and business owners
It ensures everyone agrees on the system's capabilities
Using part 20 - Vehicles and part 2 - Components with Functional Aspect
D – vehicle system designed to control angular orientation
CD – technical system designed to control fluid dynamics by dividing it by active means
CF – technical system designed to control fluid dynamics by modifying it by active means
CE – technical system designed to control fluid dynamics by merging it by active means

## Slide 18: Functional ↔ Product Link
The reference model allows anyone to understand which function is allocated to which product
FUNCTIONAL
PRODUCT

## Slide 19: Location Aspect
LOCATION
PRODUCT
Using spaces classification, it is also possible to link a product to its location

## Slide 20: The Model Tells Stories
This is because Inner spoiler 1 system is located in zone 571 (inner area) that it has High effect fluid modification capability
(while outer spoilers have medium effect…)

## Slide 21: Link to the Processes
This view conveys the fact that the Roll process is realized by the functions of medium effect fluid modification
PROCEDURAL
FUNCTIONAL
Using part 50 - Processes
E – the act of moving an entity
GAC – task for changing position of an object in space by autonomous rotation around an axis
KBC – task for supervising equipment or procedures for modification by adjusting the input

## Slide 22: Manufacturing Story Example
Long distance transport can be realized by air or water transportation system functions
Air transportation system function is allocated to Beluga fleet made of 6 Beluga XL
PROCEDURAL
FUNCTIONAL
LOGICAL
PHYSICAL

## Slide 23: Assigning Properties
Properties defines the specific characteristics or attributes of an object
Properties are directly anchored to a specific system
Properties provide a link between data and knowledge
Using part 8 - Properties

## Slide 24: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 25: How? | Connect Different Softwares

## Slide 26: How? | Connect Different Softwares

## Slide 27: How? | Speaking RDS is a Capability
Some softwares natively speak RDS…
… Others only need a text attribute that stores RDS code to speak it
How are softwares linked to the RDS?

## Slide 28: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 29: What? | Call to Software Editors
We invite software editors to join us in building an interoperable ecosystem powered by the RDS framework.
Participate in the construction of RDS Enablers

## Slide 30: What? | Call to Software Editors

## Slide 31: What? | Call to Software Editors
Manual text entries
Assisted selection through AI

## Slide 32: Agenda
Communication Kit
Why?
How?
Usecase Overview
What?
Next Steps

## Slide 33: What we will present end of Q1
RDS as an enabler of interoperability of knowledge
Status on Part 20 testing
Intermediate status on specification of missing RDS artefacts
Software – Expression of the need & Call for editor collaboration

## Slide 34
Thank you
This document and all information contained herein is the sole property of Airbus. No intellectual property rights are granted by the delivery of this document or the disclosure of its content. This document shall not be reproduced or disclosed to a third party without the expressed written consent of Airbus. This document and its content shall not be used for any purpose other than that for which it is supplied.
Airbus, its logo and product names are registered trademarks.