## Slide 1
Your test data already knows.
• WATS UP 2026 · DEEP-DIVE SESSION •
Test Step Analysis
Reading the signals your test data has been sending all along.
20 min of signals · 40 min live in WATS
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 2
Yield is just the tip
The pass/fail bit hides everything that is about to go wrong.
ABOVE THE WATERLINE — WHAT EVERYONE WATCHES
FPY, pass counts, the red/green verdict — one bit per unit.
the pass/fail waterline
BELOW — WHAT TEST STEP ANALYSIS READS FIRST
Drift — averages walking toward a limit
Leaning measurements — a population parked off-center
Excess spread — the limit window nearly full
Multiple distributions — two processes hiding in one step
Outliers — sentinels and glitches polluting the stats
Near-limit passes — passing today, failing tomorrow
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 3
• THE METHOD •
From yield to root cause
One report, four levels down — each level narrows the suspects.
Inspect the batch
UUT pass/fail on a product batch: FPY, volume, retest rate.
➜
Rank failing steps
Step pareto: which steps fail most — and which failures are decisive for the unit verdict?
➜
Correlate the config
Split by station, fixture, revision, batch, operator, SW. Who is different?
➜
Read the step
avg · min/max · σ · Cp · Cpk · WOF — the distribution against its limits.
➜
Name the cause
Process, product, or test system — with the evidence already attached.
TSA turns “yield dropped” into “this fixture, this step, this cause.”
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 4
• THE CAST •
Five families of numbers
Every KPI answers exactly one question. None of them answers alone.
Location
Where does the process sit — and how close to a wall?
avg • min / max • limits & comparator
Spread
How much does it vary, regardless of where the limits are?
stdev • variance • Cp — spread vs window
Position
Spread AND aim, measured against the limits — the headline capability.
Cpk • cpUpper / cpLower • centering
Robustness
The same indices ignoring freak values — your built-in outlier detector.
Cpk WOF • Cp WOF • the Cpk↔WOF gap
Outcome
What actually failed — and whether this step decided the unit's fate.
failure rate • caused-UUT-fail • first-run FPY
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 5
• THE ONLY FORMULA SLIDE •
Cp asks if it fits. Cpk asks if it’s aimed.
Cp: will the car fit the garage. Cpk: will it fit the way you are driving in.
CASE 1 · TOO WIDE
Spread problem
LSL
USL
Cp 0.6 — window smaller than the spread
Re-centering can't save this. Reduce variation, or fix unrealistic limits.
CASE 2 · OFF AIM
Aim problem
LSL
USL
Cp 1.6 · Cpk 0.4 — fits, badly parked
The spread is fine. Re-center, trim, or hunt the test-system offset.
CASE 3 · CAPABLE
Fits and aimed
LSL
USL
Cp ≈ Cpk ≥ 1.33 — margin both sides
The Cp–Cpk gap is pure centering — that gap is free capability.
1.00
~2 700 ppm
1.33
~63 ppm
1.67
~0.6 ppm
Cp = fit. Cpk = fit + aim. Below 1.33 — act.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 6
• THE KEY HABIT •
Never read one KPI alone
Cpk × failure rate — four squares, four completely different verdicts.
← Cpk (all)
failure rate →
Healthy
Fails rarely, wide margins. Leave it alone — and stop re-testing it into the ground.
Two populations
Fails often, yet passing units look capable. Two processes in one step — split by station / batch / component until it separates.
Ticking bomb
Zero failures, no margin. The limits swallow the whole distribution — the next small shift ships failures.
Broken
Fails often, no margin. Everyone already knows this one — TSA's job is the three squares around it.
WHY COMBINATIONS
The habit
A single KPI never diagnoses. Pairs do — and the pair tells you what to do next.
Yield sees today. Cpk sees tomorrow. Read both, always.
High Cpk with high failure rate is not a paradox — it is a second population hiding in the step.
The five signs coming next are these squares, found in live WATS data.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 7
• SIGN 1 OF 5 · AIM •
Good spread, bad aim
A 0.12% failure rate hides a process hugging its upper limit.
Green LED output voltage vs limits
Aug 2026 ⌄
PCBA Test ⌄
Reconstructed from live WATS KPIs — PN 277288 · PCBA Test · n=5 690 · avg 0.129 V · σ 0.036 V
LSL
USL
Target
Measurement
HOW TO READ IT
Cp fine, Cpk poor → aim
Cp
1.39
≥ 1.33
the spread would fit easily
Cpk
0.18
< 1.33
…but it sits at the wall
cpUpper 0.19 vs cpLower 2.60 — the asymmetry names the wall
Fix the aim: re-center, trim — or challenge the limit
Yield today: 99.9%. One drift away from a bad week.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 8
• SIGN 2 OF 5 · SPREAD •
Zero failures. Ticking bomb.
2 900 units, not one failure — and one of the worst steps in the operation.
MAX fan speed vs limits 70–100
Aug 2026 ⌄
Final Function Test ⌄
Reconstructed from live WATS KPIs — PN 758877.874 · Final Function Test · n=2 900 · avg 81.4 · σ 9.9 · 0 failures
LSL
USL
Target
Measurement
HOW TO READ IT
The limits eat everything
0 failures in 2 900 units — FPY 100%
Cp
0.49
< 1.33
spread vs window
Cpk
0.43
< 1.33
what capability sees
min = LSL, max = USL: the window is completely full
Nothing fails — until the next component lot shifts the mean
Fix the spread now, or meet this step in a crisis later
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 9
• SIGN 3 OF 5 · OUTLIERS •
Same ugly Cpk — opposite diagnosis
Two ICT steps, both catastrophic on paper. The WOF gap is the tiebreaker.
T101_1_2 · TRANSFORMER WINDING
Cpk −0.03 …but WOF 5.56 · fails 1.4%
LSL
USL
sentinel readings → “99 999”
The TEST misfires — the product is perfect.
Open readings logged as 99 999 wreck avg and σ. Remove them and Cpk is 5.6 — fix contact & sentinel logging, don't chase boards.
NTC101 · THERMISTOR
Cpk −0.01 …and WOF 0.66 · fails 3.8%
LSL
USL
a few glitches — but the curve is the problem
The PROCESS is wide — 111 boards really failed.
Even with outliers removed it cannot hold 40–120 Ω. Top decisive failure of the whole ICT — a genuine capability problem.
The WOF gap decides: WOF fixes it → fix the test. WOF doesn’t → fix the process.
Live WATS data — PN 4494394418 · ICT test · Aug 2026
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 10
• SIGN 4 OF 5 · MIXTURES •
One histogram, four processes
The “process spread” of this step is mostly four stations disagreeing.
+3.3 V supply current by station
Aug 2026 ⌄
PCBA Test ⌄
Live WATS data — PN 277288 · PCBA Test · Aug 2026 · per-station avg/σ from step comparison
LSL 5 mA
USL 130 mA → far off-screen
0
20
40
60
80
+3.3 V supply current (mA)
— C-002 (σ 8.4) — A-008 (σ 14.8) — E-001 (σ 10.9) — E-002 (σ 2.0) --- the aggregate
HOW TO READ IT
σ across ≠ σ within
Aggregate σ 14.4 — looks like a hopeless process
Station averages: 16 · 37 · 39 · 52 mA — four processes
E-002 runs σ 2.0: the product CAN do it
Align the stations before touching the product
Rule: group by station / fixture / rev BEFORE judging spread.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 11
• SIGN 5 OF 5 · TIME •
Numbers that move
The aggregate said “stable”. The time axis said otherwise.
Slow drift
wear, aging, contamination
Step change
new calibration, SW, batch, limit
Oscillation
station mix, temperature, shifts
Measure Vout @ 95 VAC — biweekly avg and Cpk
Jun–Sep ⌄
Final Function Test ⌄
Live WATS data — PN 758877.874 · Final Function Test · biweekly buckets, Jun–Sep 2026
avg (V)
53.6
53.7
53.8
USL 54.00 ↑ · LSL 53.00 ↓ (zoomed view)
Cpk
1.33
1.95
0.73
6.39
0.79
0.67
0.90
0.67
Jun 1
Jun 15
Jun 29
Jul 13
Jul 27
Aug 10
Aug 24
Cpk swings 6.4 → 0.67 while the mean steps 53.64 → 53.77 V. Trend view answers WHEN — the dimension split answers WHO.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 12
• ALL FIVE LEVELS, ONE CASE •
The hunt, start to finish
A real month of production — and the demo we are about to run live.
1
Inspect the batch
•
2 936 units, one month
•
FPY 88% — a yield tax
•
retests piling up
UUT level
2
Rank failing steps
•
Vout @ 95 Vac tops the list
•
2.4% fail — every one decisive
•
failed readings near zero volts
step level
3
Split by station
•
Z-970: 10.6% fail · Cpk 0.06
•
sister stations: 0% · Cpk ≈ 5
•
same step, same product
dimension level
4
Corner the fixture
•
fixtures #70–72 implicated
•
~94% of the fails are false
•
boards were fine all along
root cause
Root cause isolated without touching a single board — and it was never the board.
Live WATS data — PN 4494394418 · PCBA Test · Aug 2026 · station WVXM-NGH-Z-970
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 13
• FIELD NOTES •
Tips & tricks
The habits that keep the numbers honest.
Before you trust a number
1
First runs only
Retests flatter every statistic. WATS defaults to run 1 — keep it that way for capability.
2
Enough samples
Cpk from fewer than ~30 units is a rumor. Check volume before narrowing the date range.
3
Numeric steps only
Cp/Cpk exist for numeric-limit steps. PassFail and string steps only have a failure rate.
4
Mind the sentinels
99 999-style error codes destroy avg and σ. Log a fail, not a magic number.
Before you blame the process
1
Split before you judge
Station, fixture, SW, batch first — much “process drift” is one machine.
2
Check the WOF gap
If removing outliers fixes the index, hunt the test system, not the product.
3
One limit → one side
GE/LE steps: read cpLower or cpUpper. A two-sided Cp is meaningless there.
4
Trim steps lie
Post-trim Cpk is centered by design. Judge trim steps on Cp — or on pre-trim data.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 14
• PHOTOGRAPH THIS ONE •
The cheat sheet
Symptom → KPI signature → likely cause → first move.
SIGN
KPI SIGNATURE
LIKELY CAUSE
FIRST MOVE
1
Off aim
Cp OK · Cpk low · cpUpper ≠ cpLower
process shifted toward one limit
re-center / trim; check test-system offset
2
Too wide
Cp low · Cpk ≈ Cp · WOF ≈ same
genuine process variation
attack variation; sanity-check the limits
3
Outliers
Cpk WOF ≫ Cpk
sentinels, contact & fixture glitches
fix the test; log fails, not 99 999
4
Two populations
failure rate high · Cpk (pass) decent
config / component / station split
split by dimension until it separates
5
On the move
avg or Cpk trending / stepping in time
wear, calibration, SW or batch change
trend view for WHEN; dimensions for WHO
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 15
• THE 30-SECOND METHOD •
Five numbers, in order
For any suspicious step — this sequence, every time.
1
Failure rate + caused-UUT-fail
Is this step hurting yield — and is it the decisive failure?
2
Cpk (all)
How much margin does the whole population really have?
3
Cpk vs Cpk WOF
Outliers or true spread? The gap is the tiebreaker.
4
Cp vs Cpk
Too wide — or just badly aimed?
5
Trend + split by dimension
When did it change, and which station / fixture / batch is different?
Thirty seconds per step. That is the whole method.
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis

## Slide 16
Over to WATS →
• AND NOW — LIVE •
Let’s read live data
The same five signs, found in minutes on the Test Step Analysis report.
Demo: TSA on this month’s production
Ola Lund Reppe — WATS
WATS UP 2026 · Test Step Analysis