## Slide 2
This presentation is for use with
“Lesson Plan: Household Membrane Filters”
in the Household Water Treatment and Safe Storage (HWTS) Trainer Manual
Available at resources.cawst.org

## Slide 3
Household Membrane Filters
2018
June

## Slide 4: Have You Used Membrane Filters?

## Slide 5: Learning Outcomes
Explain what membrane filters are
Describe different membrane filter cartridges and setups
Describe some of the limitations of membrane filters

## Slide 6: What Are Membrane Filters?
Membrane: Any type of material with tiny holes (pores) that allow fluids to pass through but prevent the passage of certain particles or chemicals
Membrane filters: Devices that contain a membrane and use a driving force (such as gravity or pumping) to push water through the membrane

## Slide 8: Types of Membrane Filters
Membrane filters differ in:
Pore size
Membrane cartridge configuration
Container setup

## Slide 9: Pore Size or Particle Size
Membrane Type |  |  |  |  |  | 
Particle Type |  |  |  |  |  | 
0.1 nm
1 nm
10 nm
100 nm
1 micron
10 microns
Smaller
Bigger
Reverse
Osmosis
Nanofiltration
Ulrafiltration
Microfiltration
Salts, Metal Ions
Pesticides
Proteins
Viruses
Bacteria
Protozoa
Helminths

## Slide 10: Membrane Cartridge Configuration
Large Tube Membrane
Water moves through the pores of the tube wall (membrane).

## Slide 11: Membrane Cartridge Configuration
Spiral-Wound Membrane
Water moves into the cartridge and travels through wrapped layers of membrane to reach a central tube.

## Slide 12: Membrane Cartridge Configuration
Hollow Fibre Membrane
Water moves into the cartridge and travels through tiny pores into the hollow fibres.

## Slide 13: Container Setup: Tabletop (Gravity Driven)

## Slide 14: Container Setup: Hanging (Gravity Driven)

## Slide 15: Container Setup: Pump Driven

## Slide 16: Considerations and Limitations
Highly variable designs to choose from (different volume, pore size, configuration)
Trade-off between microbiological performance and flow rate
Lifespan: manufacturer-stated vs. real conditions
What’s needed for backwashing, repair, and replacement
Potential for membrane fouling and membrane rupture

## Slide 17: Review: Group Discussion
1. Given what you learned in this lesson, how would you categorize your filter? Consider:
      Pore size (ultrafiltration or microfiltration)
      Membrane configuration (your best guess)
      Filter setup
2. Would you use this filter? Why or why not?
(Membrane Fact Sheets)