## Slide 1
12, 2916 – 5th Avenue
Calgary, Alberta, T2A 6K4, Canada
Phone: + 1 (403) 243-3285, Fax: + 1 (403) 243-6199
E-mail: cawst@cawst.org, Website: www.cawst.org
CAWST, the Centre for Affordable Water and Sanitation Technology, is a nonprofit organization that provides training and consulting to organizations working directly with populations in developing countries who lack access to clean water and basic sanitation.
One of CAWST’s core strategies is to make knowledge about water common knowledge. This is achieved, in part, by developing and freely distributing education materials with the intent of increasing the availability of information to those who need it most.
This document is open content and licensed under the Creative Commons Attribution Works 3.0 Unported License. To view a copy of this license, visit http://creativecommons.org/licenses/by/3.0 or send a letter to Creative Commons, 171 Second Street, Suite 300, San Francisco, California 94105, USA.
You are free to:
        Share – to copy, distribute and transmit this document
        Remix – to adapt this document
Under the following conditions:
        Attribution. You must give credit to CAWST as the original source of the document. Please include our website: www.cawst.org
CAWST will produce updated versions of this document periodically. For this reason, we do not recommend hosting this document to download from your website.
CAWST and its directors, employees, contractors, and volunteers do not assume any responsibility for and make no warranty with respect to the results that may be obtained from the use of the information provided.
Stay up-to-date and get support:
            Latest updates to this document
            Other workshop & training related resources
            Support on using this document in your work
CAWST provides mentorship and
coaching on the use of its education
and training resources.

## Slide 2
This presentation is used with Lesson Plan 6: Intro to Microbiological Testing in the Drinking Water Quality Testing Trainer Manual
Available at www.cawst.org/resources

## Slide 3: Introduction to Microbiological Testing Methods

## Slide 4: Learning Expectations
1. Identify 3 microbiological test methods: presence-absence, most probable number, and membrane filtration.
2. Discuss the advantages and limitations of different microbiological test methods.

## Slide 5: Microbiological Testing Methods
Presence-Absence (P-A)
Most Probable Number (MPN)
Membrane Filtration
Notes: Three methods to determine the presence of indicator bacteria in drinking water.

## Slide 6: Presence-Absence (P-A)
Positive for
E. coli
Negative
Positive for Coliforms
Black water is positive result for H2S bacteria and likely fecal contamination
Notes: There are different P-A tests that use total coliform and/or E. coli as the indicators. The general process for these tests is:
  A powdered reagent is added to the water sample
  The sample is incubated for 24-48 hours at 35oC
  The results are read: Colourless = negative, Colour = total coliforms present, Fluorescent = E. coli present (tested with a UV lamp)
There are different P-A tests using H2S bacteria that are produced by different manufacturers. For example, in the P-A test manufactured by ENPHO in Nepal, a strip of test paper is added to a water sample. If the test paper turns black within 24 hours, it means that H2S was produced, which means that bacteria coming from feces are likely present in the water sample.

## Slide 7: Presence-Absence (P-A)
Simplest method
Does not show numbers of bacteria!
If positive results, water should be re-tested using membrane filtration to determine the number of bacteria
Not recommended for testing treatment effectiveness of household water treatment and safe storage
Notes:   P-A tests are generally only appropriate in circumstances where thermotolerant coliforms are rarely found and when contamination occurs only at low levels (e.g., in deep wells).
  P-A testing is not appropriate for testing the treatment effectiveness of HWT technologies. We already know that many of these technologies may not be 100% effective for bacteria removal, so there is a chance that P-A tests will turn positive when testing the treated water.

## Slide 8: Most Probable Number (MPN)
# Positive Tubes | MPN Index (CFU/100 mL)
0 | <1.1
1 | 1.1
2 | 2.2
3 | 3.6
4 | 5.1
5 | 6.9
6 | 9.2
7 | 12.0
8 | 16.1
9 | 23.0
10 | >23.0
Example Table for 10 Test Tubes
Multiple wells in a
disposable tray (1 mL each)
Notes: Estimates the number of indicator bacteria that is most likely to be present in the water sample.
Multiple samples (1-10 mL) of the same water to be tested are added to a culture media in sterile tubes and incubated at a particular temperature for a fixed time (usually 24 hours). Three or five tubes are commonly used, though ten tubes may be used for greater sensitivity.
Becoming more popular to use a disposable tray with multiple small wells instead of multiple tubes since it simplifies the procedure.
By counting the number of tubes or wells showing a positive result, and comparing with a standard table, a statistical estimate of the most probable number of bacteria can be made. The results are reported as MPN per 100 mL.

## Slide 9: Most Probable Number (MPN)
Estimates number of bacteria most likely to be in water sample
Procedure:
  Add water to 5-10 test tubes (or trays of 10–96 wells) containing culture media
  Incubate for 24-48 hours
Statistical method based on the number of positive tubes or wells
  Using a table provided, the number of positive tubes is reported as the MPN /100 mL
Notes: The most probable number (MPN) test method estimates the number of indicator bacteria that is most likely to be present in the water sample.
Multiple samples (1–10 mL) of the same water to be tested are added to a culture media in sterile tubes and incubated at a particular temperature for a fixed time (usually 24 hours). Three or five tubes are commonly used, though ten tubes may be used for greater sensitivity.
It is becoming more popular to use a disposable tray with multiple small wells instead of multiple tubes since it simplifies the procedure. By counting the number of tubes or wells showing a positive result, and comparing with a standard table, a statistical estimate of the most probable number of bacteria can be made.
The results are reported as MPN per 100 mL

## Slide 10: Membrane Filtration (MF)
Credit: WHO, 2007

## Slide 11: Membrane Filtration (MF)
Most accurate and internationally recognized method
Procedure:
  Filter 100 mL water sample
  Add culture media to a Petri dish to provide nutrients for indicator organisms to grow
  Transfer the membrane filter paper to Petri dish
  Incubate for 24-48 hours
Colonies will appear on filter paper and can be counted
Results reported as colony forming units per 100 mL of water sample (CFU/100 mL)
Notes: Membrane filtration can be done in a laboratory or by using a portable test kit.
The size and colour of the colonies depends on the type of bacteria and culture media used.
The bacteria colonies are counted to determine the number of colony forming units (CFU) per 100 mL.
MF has limitations, particularly when testing waters with high turbidity or large numbers of noncoliform (background) bacteria.
Turbidity caused by the presence of algae or suspended particles can clog the membrane or prevent the growth of indicator bacteria on the filter paper. Need to dilute the water sample.

## Slide 12: Portable Field Kits
Credit: Palintest, no date
Notes: Different portable field test kits are available for membrane filtration including:
Palintest (Wagtech) and Delagua kits

## Slide 13: Portable Incubator
Notes: Important piece of equipment needed for membrane filtration, and sometimes for P-A and MPN tests.
Different types of incubators made by different manufacturers. Some incubators are portable and use a battery for power supply, while others need to stay in one location and use the main power supply.
Incubation temperature is critical to ensure that microbiological test results are accurate. Different culture media require different temperatures to grow the specific indicator bacteria.
Incubators need to be calibrated on a regular basis to make sure that the temperature is accurate.

## Slide 14: Disposable Membrane Filtration Equipment
Credit: Micrology Labs, no date
Notes: One brand is Nalgene but others are available

## Slide 15: What are the Advantages and Limitations?
Presence Absence (P-A)
Most Probable Number (MPN)
Membrane Filtration (MF)
Notes: Ask participants to suggest advantages and limitations before discussing them.
P-A Advantages: 1. Simple to understand & use; 2. Rapid results (within 24 hours); 3. Doesn’t require extensive equipment; 4. Portable and durable in field; 5. Relatively inexpensive
P-A Disadvantages: 1. Does not show how many bacteria are in the sample; 2. Not recommended by WHO for analysis of surface water and untreated community water supplies; 3. Not recommended for testing the efficiency of household water treatment technologies (e.g., biosand filter)
MPN Advantages: 1. Quantitative results; 2. Simple to understand and use; 3. Relatively inexpensive; 4. Can be used with turbid water
MPN Disadvantages: 1. More labor intensive than P-A; 2. Requires some training; 3. Requires incubator & other equipment; 4. Disposable trays generate a lot of waste
MF Advantages: 1. Able to count the number of bacteria; 2. Most accurate test method; 3. Internationally recognized method; 4. Ability to test many samples at once
MF Disadvantages: 1. More labour intensive than MPN, P-A; 2. Requires more training; 3. Requires additional equipment; 4. Cost of consumables can be high in many countries; 5. More difficult to use with turbid water (dilution required)