DIVISION 12 00 00					FURNISHINGS

SECTION 12 93 00					SITE FURNISHINGS

SECTION 12 93 13					BICYCLE RACKS

ELEVEN BIKE RACK

Part 1		General

- Summary

  - Section Includes:

    - Surface mount bike rack:

      - 34.38" high bike rack with stainless steel body.

    - Cast-in-place bike rack:

      - 34.38" high bike rack with stainless steel body.

- Submittals

  - Provide submittals in accordance with Section 01 33 00 – Submittal Procedures.

  - Product data:

    - Manufacturer’s standard product literature.

    - Shop drawings.

    - Installation instructions.

    - Maintenance instructions.

  - Submit powdercoat finish samples for approval.

- Quality Assurance

  - Manufacturer Qualifications:

    - Minimum 15 years experience in the manufacture of site furnishings and amenities.

    - Provide reference list of at least ten major transportation authorities, municipalities, universities, or other high-use public environments currently using site furnishings and amenities fabricated by the manufacturer.

- Delivery, Storage and Handling

  - Handle products in accordance with manufacturer’s instructions.

  - Store products in manufacturer’s original packaging until ready for installation.

  - Protect products from impacts and abrasion during storage.

- Warranty

  - Provide manufacturer’s standard warranty:

    - Warranty terms: three years from date of invoice against defects in materials and workmanship.

Part 2		Products

- Manufacturer

  - Basis-of-design product: 	provide bike racks based on the product named:

    - Eleven Bike Rack by Forms+Surfaces.

    - Manufacturer Contact:
Forms+Surfaces
30 Pine Street
Pittsburgh, PA 15223
phone: 800-451-0410

fax: 412-385-4715

email: sales@forms-surfaces.com

website: www.forms-surfaces.com

  - Bike Racks

    - Materials:

      - Tubular element: stainless steel tubing.

      - Top plate: stainless steel.

      - Base plate (surface mount models only): stainless steel.

      - Hardware: stainless steel.

    - Finishes (Choose either stainless steel or powdercoat from below):

      - Surface mount:

        - Tubular elements & base plate (Choose either stainless steel or powdercoat from below):

            - Stainless steel with Satin finish.

            - Polyester powdercoat (Select one option below):

              - Standard Texture from Forms+Surfaces Powdercoat Chart.

              - Custom RAL powdercoat color.

        - Top plate (Choose either stainless steel or powdercoat from below):

            - Stainless steel with Satin finish.

            - Polyester powdercoat (Select one option below):

              - Standard Texture from Forms+Surfaces Powdercoat Chart.

              - Custom RAL powdercoat color.

      - Cast-in-place:

        - Short tubular element (Choose either stainless steel or powdercoat from below):

            - Stainless steel with Satin finish.

            - Polyester powdercoat (Select one option below):

              - Standard Texture from Forms+Surfaces Powdercoat Chart.

              - Custom RAL powdercoat color.

        - Tall tubular element (Choose either stainless steel or powdercoat from below):

            - Stainless steel with Satin finish.

            - Polyester powdercoat (Select one option below):

              - Standard Texture from Forms+Surfaces Powdercoat Chart.

              - Custom RAL powdercoat color.

        - Top plate (Choose either stainless steel or powdercoat from below):

            - Stainless steel with Satin finish.

            - Polyester powdercoat (Select one option below):

              - Standard Texture from Forms+Surfaces Powdercoat Chart.

              - Custom RAL powdercoat color.

    - Dimensions (Choose model(s) from below):

      - Surface mounted bike rack:

        - 34.38" high, 24.75" wide, 3.25" deep, 2.5" diameter tube.

      - Cast-in-place bike rack:

        - 44.38" high overall, 34.38" above-ground height, 24.75", 3.25" wide, 2.5" diameter tube.

    - Mounting: (Choose mounting option below):

      - Surface mount with embedded anchors. Stainless steel anchors and tamper-resistant stainless steel bolts are sold separately.

      - Cast-in-place.

Part 3		Execution

- Examination

  - Verify that substrates are stable and capable of supporting the weight of items covered under this section.

  - Verify that substrates have been adequately prepared to securely anchor those items that will be surface mounted.

- Installation

  - Install according to the manufacturer’s installation instructions.

  - Install in conformance to applicable ADA guidelines and End User’s established Accessibility policies.

END OF SECTION